Идет перевод…

Open HTTP API Methods, v1.17

Table of contents

	returnGroupes	2

	returnPlayStatus	2

	returnReport	3

	initSmartSNR	6

	startEvents	9

	factoryDefaults	9

	clearChannelList	9

	version	9

	sleepStb	10

	returnSATList	11

	returnTPList	12

	createReport	14

	scanChannels	15

	updateConfig - HTTP POST	16

	smartcardInfo	18

	channelList	21

	getConfig	23

	upgradeSoftware - HTTP POST	23

	commonEvent	24

	formatEmbeddedPartition	24

HTTP URL: `http://stb_ip/public`, GET request

- returnGroupes

Returns a list of satellites with scanned channels. Used to create a link for the player.

| Reply field | Description |
| --- | --- |
| stblink | the title of the channel list address for the player |
| groupes | channel list array : ["field0", "field1"] , where "field0" is the name of the satellite, "field1" is the name of the list |

Example: http://192.168.1.56/public?command=returnGroupes

Answer :

{

"stblink": "http://192.168.1.56/stream/",

"groupes": [

[

"All Channels",

"All_Channels_ID_65535.m3u"

],

[

".NTV Plus",

". NTV_Plus_ID_404.m3u"

]

]

}

The final link to the channel list for viewing satellite ".NTV Plus" through an external program: http://192.168.1.56/stream/.NTV_Plus_ID_404.m3u

- returnPlayStatus

Start playing a video link through the built-in IPTV player.

| Parameter field | Description |
| --- | --- |
| PlayLink | address for the IPTV player (file format ts/mp4/m3u) |

Example:

http://192.168.1.56/public?command=returnPlayStatus&PlayLink=https://kinogo.tv/deep_mide.m3u

- returnReport

Returns satellite scan report in json format.

| Parameter field | Description |
| --- | --- |
| report_name | the name of the binary report file with the replacement of extension to json |

| Reply field | Description |
| --- | --- |
| date | report creation date |
| version | object with firmware information |
| current | object with current firmware version information |
| software | software version |
| web_api | web interface API version |
| base_struct | data structure version |
| report | object with actual firmware version information |
| software | software version |
| web_api | web interface API version |
| base_struct | data structure version |
| serial | receiver serial number |
| sat_position | satellite position |
| sat_name | satellite name |
| tp_num | the number of frequencies used for the report |
| lnb_info | object with information about satellite settings : |
|  | type | converter type: 0 - standard, 1 - custom, 2 – universal |
|  | low_freq | lower local oscillator frequency , MHz |
|  | high_freq | upper local oscillator frequency , MHz |
|  | dsq1.0_port | DISEQC version 1.0 port number, values : 1-4 , 0 - disabled |
|  | dsq1.1_port | DISEQC version 1.1 port number, values : 1-16 , 0 - disabled |
|  | positioner_type | 0 no positioner 1 DiSEqC1.2 positioner 2 USALS positioner |
|  | tone | tone sending: 1 - on, 0 - off |
| lnb_3d | object with 3D converter parameters |
| hw_version | hardware version |
| sw_version | software version |
| lnb_v | voltage vertical polarization |
| lnb_v22 | vertical polarization voltage with tone enabled |
| lnb_h | horizontal polarization voltage |
| lnb_h22 | horizontal polarization voltage with tone enabled |
| alfa | tilt angle, the X axis, degrees; 360.0 means no 3D converter is connected |
| beta | tilt angle, the Y axis, degrees |
| gamma | tilt angle, the Z axis, degrees |
| correction | object with calibration values |
| alfa | the X axis, degrees |
| beta | the Y axis, degrees |
| gamma | the Z axis, degrees |
| ripples | object with maximum ripple amplitude |
| alfa | the X axis, degrees |
| beta | the Y axis, degrees |
| gamma | the Z axis, degrees |
| user |  |
| user_longtitude | longitude of the dish installation: “N” for >= 0, “S” for < 0 |
| user_altitude | latitude of the dish installation: “E” for >= 0, “W” for < 0 |
| lnb_3d_serial | 3D LNB serial number (10 characters) |
| dish |  |
| vendor | dish manufacturer |
| model | dish model |
| diameter | dish size, sm |
| offset | dish elevation offset, it is individual for each model, degrees |
| user | 0 – dish from presets; 1 - the dish is added into the base by the user and the offset is measured; 2 - the dish is added into the base by the user and offset is not measured |
| stats | list of objects with report statistics |
| avr_h_pwr | average power on horizontal polarization |
| h_tp_num | number of frequencies used to calculate avr_h_pwr |
| avr _ v _ pwr | average power at vertical polarization |
| v _ tp_num | number of frequencies used to calculate avr _ v _ pwr |
| rssi_db | list of objects with rssi statistics, signal in dBuV |
|  | average | mean rssi |
|  | tp_used | number of frequencies to calculate |
|  | min | minimum rssi value |
|  | tp_idx | reference to the transponder number in the table |
|  | freq | frequency, MHz |
|  | sr | symbol rate |
|  | polarity | polarization: 0 - horizontal, 1 - vertical |
|  | nim_type | broadcast standard: DVBS or DVBS2 |
|  | max | maximum rssi value |
|  | tp_idx | reference to the transponder number in the table |
|  | freq | frequency |
|  | sr | flow rate |
|  | polarity | polarization: H - horizontal, V - vertical |
|  | nim_type | broadcast standard: DVBS / DVBS2 |
|  | divergence | difference between max and min signals |
| cn_db | list of objects with statistics of signal quality in dB |
| lm_cn_db | list of objects with statistics of signal link margin in dB |
| common_param | list of frequencies with measurements of signal parameters |
| idx | index of the transponder in the report table |
| freq, sr, polarity, nim_type | see description in rssi_db |
| offset | carrier offset, MHz |
| lnb_v | LNB supply voltage measured by the receiver |
| lnb_ma | measured by the receiver LNB current consumption |
| fec | FEC: "1/4", "1/3", "2/5", "1/2", "3/5", "2/3", "3/4", "4/5" , "5/6", "7/8", "8/9", "9/10" |
| mod | signal modulation: "QPSK", "8PSK", "16PSK", "32PSK" |
| std | broadcasting standard: "DVBS" or "DVBS2" |
| rssi | signal level, dBuV |
| cnr | signal/noise ratio (quality), dB |
| lm_cnr | signal margin, dB |
| per | packet errors |
| result | transponder test result: |
|  | OK | no error, signal ok |
|  | BAD | No signal |
| spectrum_crc | spectrum checksum result |
|  | CRC_OK | no data error |
|  | CRC_ERROR | error in measurement data |
| spectrum_band_points | the number of points in each of the four spectrum_data arrays |
| spectrum_data | a list with four possible signal parameters: vertical polarization without tone, vertical polarization with tone, horizontal polarization without tone, horizontal polarization with tone. |
| ret_code | 'RPT_NO_ERR' - no errors when generating the report |

Example: the stored report link http://192.168.1.55/mnt/flash/e/ls.json

Answer :

{

"partition": "e",

"dir_list" : [

{

"name": "rpt_1_850E_2021-01-07_11_09_24.bin",

"size": 912

},

{

"name": "rpt_2_850E_2021-01-07_11_10_28.bin",

"size": 912

},

{

"name": "rpt_3_585E_2021-01-07_11_14_58.bin",

"size": 296

}

],

ret_code": "FS_NO_ERR",

"files": 3,

"free_space": 252004

}

Final link to json report rpt _3_585 E _2021-01-07_11_14_58.bin:

http://192.168.1.56/public?command=returnReport&report_name=e:/rpt_3_585E_2021-01-07_11_14_58.json

Report example - report_example.json

- initSmartSNR

Change of the signal parameters monitoring mode with switching to the specified frequency. After working with the receiver in one of the three modes, it is necessary to turn off the current mode - state = off, or the receiver, after a certain timeout, will turn it off automatically, but until the mode is turned off, it will be impossible to control the frequency switching from the receiver's menu.

| Parameter field | Description |
| --- | --- |
| state | ' on ' - enable the mode; ' off ' – disable (you can skip other parameters) |
| mode | operating modes: |
|  | snr | signal and quality parameters |
|  | spectrum | spectrum at a given frequency |
|  | blindscan | blind scan at a given frequency |
| freq | tuner tuning frequency (IF), MHz |
| sr | symbol rate, but for "spectrum" mode is 63000 |
| pol | polarization: 0 - horizontal, 1 - vertical |
| tone | tone: 1 - tone on, 0 - off |
| diseqc_hex | Send DISEQC command in HEX format. Commands must be separated by commas without spaces. Example: “E01038F0,W15,E01039F0,E01038F3”. W15 means 15ms delay. The maximum string length is 128 characters. |
| smart_lnb_enabled | 3D converter polling: 1 - enabled, 0 - disabled |
| dmd | demodulator: 0 – DVBS/S2, 1 – DVBT/T2, 2 - DVBC, if not mentioned then DVBS/S2 |
| t2mi | 0 – stream autodetect (by default), 1 – t2-mi is on |
| t2mi_pid | manual PID setting for t2mi = 1 |
| plp_id | PLP id for DVBT2 or T2MI. By default automode is 256 for t2mi plp_id, 0 – for DVBT2 |
| modulation | DVBC modulation: 16 – QAM16, 32 – QAM32, 64 – QAM64 (by default), 128 – QAM128, 256 – QAM256 |

A complete list of fields in three modes, but not all of them are transmitted in the selected mode.

| Status field | Description |
| --- | --- |
| lock | signal lock: 1 - locked, 0 - not locked |
| tune_mode | the operating mode specified by the “mode” parameter field: |
|  | 0 | snr |
|  | 1 | spectrum |
|  | 3 | blindscan |
| carrier_offset | carrier offset, kHz |
| snr | signal quality, dB |
| lm_snr | link margin, dB |
| alfa | tilt angle of the 3D LNB, the X axis, degrees; 360.0 means no 3D converter is connected |
| beta | tilt angle of the 3D LNB, the Y axis, degrees |
| gamma | tilt angle of the 3D LNB, the Z axis, degrees |
| version | converter version : bits [15-8] - hardware version, bits [7-0] - software version “0000” – 3D converter not connected |
| lnb3d_voltage | supply voltage measured in the smart converter |
| lnb_current | LNB current consumption, mA |
| lnb _ voltage | LNB supply voltage measured by the receiver, mV |
| psu_voltage | power supply voltage measured by the receiver, mV |
| t2mi_plp | list of found t2mi stream plp_id, if any exist |
| tt2_plp_id | current terrestrial signal PLP index |
| tt2_plp | list of found terrestrial signal PLP indexes |
| tt2_attributes | additional parameters of the terrestrial signal: |
| code_rate | Signal FEC |
| fft | FFT mode |
| guard_interval | guard interval |
| pilot | pilot signal (only for dvbt2) |
| modulation | modulation mode |
| scan_status | signal lock status and get data status: |
|  | SCAN_WAITING_LOCK | pending capture |
|  | SCAN_WAITING_DATA | waiting for satellite data |
|  | SCAN_ALREADY_SEND | the data has already been sent to the user |
|  | NIT_PAUSED | receiving network information suspended |
|  | NIT_WAITING_DATA | waiting for network information (NIT) |
|  | NIT_ALREADY_SEND | NIT data has already been sent to the user |
|  | SCAN_DONE | SDT scan finished |
|  | NIT_DONE | NIT data received |
| service_data | object with transponder service data |
| channel_num | number of channels |
| original_network_id | unique network identifier |
| stream_id | stream id |
| channel_list | transponder channel list |
|  | provider | provider name, unicode format |
|  | name | channel name, unicode format |
|  | scrambled | 1 - the channel is encrypted, 0 - opened |
|  | sid | channel id |
| nit_data | object with transponder broadcasting network data |
| nit_name | ascii network name |
| tp_num | number of frequencies in the current section |
| network_id | network identifier, unique within the geographic region defined by the country_code parameter (https://www.dvbservices.com/country_codes/ ) |
| section_number | section number |
| last_section_number | last section number |
| tp_list | frequency list |
| service_num | reserved, 0x41 |
| stream_id | stream id |
| freq | 32-bit frequency field consisting of 4-bit BCD values. Example: “01232206” = 12322MHz |
| polarization | polarization: |
|  | 0 | linear - horizontal (H) |
|  | 1 | linear - vertical (V) |
|  | 2 | circular - left (not used in the API ) ( L ) |
|  | 3 | circular - right (not used in the API ) ( R ) |
| symbol_rate | A 28-bit character bit rate field consisting of 4-bit BCD values. Example: “00275000” = 27500Ms/s. |
| modulation_type | modulation type: 0 - " Auto " , 1 - QPSK , 2 - 8PSK , 3 - " 16-QAM " |
| modulation_system | 0 - DVBS, 1 - DVBS2 |
| fec_inner | FEC : 0 - undefined, 1 - "1/2", 2 - "2/3", 3 - "3/4", 4 - "5/6", 5 - "7/8", 6 - " 8/9 ", 7 -" 3/5 " , 8 -" 4/5 ", 9 -" 9/10 ", 15 - no FEC , values 10 - 14 are reserved |
| orbital_position | 16-bit satellite orbital position field, consisting of 4-bit BCD values. Example: “0360” = 36.0 degrees |
| west_east_flag | “ E ” - eastern part of the orbit , “ W ” - western |
| spectrum_array | array of spectrum measurements in dB, 480 points |
| blind_scan_progress | blind search progress: |
|  | 0 | frequency found |
|  | 1 | signal locked |
|  | 2 | signal not locked |
|  | 3 | search started |
|  | 4 | search is over |
|  | 6 | search interrupted |
| tp_num | the current number of found frequencies |
| tp_list | frequency list |
| rf_frequency | intermediate frequency, MHz |
| tp_sr | symbol rate, Msymbol/s |

Example: http://192.168.1.56/public?command=initSmartSNR&state=on&mode=spectrum&freq=1231&sr=63000&pol=1&tone=0&diseqc_hex=E01038F0 or without using the diseqc_hex, if not necessary to control by DISEQC protocol.

See snr_status_examples.json for an example of status in “snr” mode.

- startEvents

Start signal monitoring in accordance with the selected mode by initSmartSNR command. The event stream is opened and the receiver constantly sends the current signal state, depending on the mode. This mode requires the web page script to restart this method automatically after disconnecting.

| Reply field | Description |
| --- | --- |
| ret_code | "ONE_CLIENT_ALLOWED_ERR " - if more than one client is running with this method |

Example: http://192.168.1.56/public?command=startEvents

- factoryDefaults

Resetting the receiver to factory defaults.

Example: http://192.168.1.56/public?command=factoryDefaults

- clearChannelList

Erase all channels.

Example: http://192.168.1.56/public?command=clearChannelList

- version

Obtaining the firmware and internal data structures version.

| Reply field | Description |
| --- | --- |
| ret_code | method error code: NO_ERR - no errors KEY_PRESSED_ERR – RCU button pressed |
| stb_name | the name of the receiver to find it on the network |
| version | version object: |
|  | stb | receiver version |
|  | web_api | web interface API version |
|  | base_struct | in the version of data structures : “base.status.satellites.frequencies.programs” |
|  | comment | base_struct fields description |
| card_inserted | Is the card inserted and initialized? : “true” - inserted, “false” - not inserted |
| channels_exist | Are there channels in the receiver? : “true” - there are, “false” - no channels |
| streaming_channel | “true” - viewing from the remote device is enabled, work with Web API is limited; “false” – no streaming, works with Web API without any limits. In case of restrictions, the “ret_code” field will contain the value “STREAMING_ERR”. |

Example: http://192.168.1.56/public?command=version

Answer:

{

"ret_code": "NO_ERR",

"version": {

"stb": "SR508HD 1.21 16.03.2021",

"web_api": "1.14",

"base_struct": "01.01.01.01.01.04",

"comment": "base , status, sat, tp , pg, rpt"

},

"card_inserted": "false", "channels_exist": "true"

}

- sleepStb

Switching the receiver to power saving mode and back.

| Parameter field | Description |
| --- | --- |
| state | Power saving mode status: “ On ” - enabled; “ Off ” - disabled. |

Example: http://192.168.1.56/public?command=sleepStb&state=on

- returnSATList

Request a list of satellites.

| Reply field | Description |
| --- | --- |
| ret_code | method error codes: |
|  | DB_NO_ERR | read from the database without errors |
|  | SYS_MEM_ERR | no memory for json text |
| sat_num | number of satellites in the list |
| sat_list | satellite list |
| sat_degree | satellite position, degrees |
| direction | direction to the satellite: 'E' - east , 'W' - west |
| lnb_type | converter type: |
|  | 0 | standard |
|  | 1 | custom |
|  | 2 | universal |
| lnb_low_freq | lower local oscillator frequency, MHz |
| lnb_high_freq | upper local oscillator frequency, MHz |
| sat_name | user defined satellite name |
| sat_id | unique internal satellite number |
| sat_mode | 0 – satellite signal, 1 – terrestrial, 2 – cable |
| t2_sat | 0 – satellite signal, 1 – terrestrial signal |
| country_id | country number for terrestrial signal search only |
| tone | tone 22kHz : 1 - on, 0 - off |
| v12 | output (option) 12V: 1 - on , 0 - off |
| diseqc10_port | DISEQC version 1.0 port number, values: 1-4, 0 - "disabled " |
| motor_position | DiSEqC 1.2 positioner position index |
| diseqc11_port | DISEQC version 1.1 port number, values: 1-16 , 0 - "disabled" |
| lnb_power | LNB power supply: |
|  | 0 | auto 13/18V |
|  | 1 | 13B |
|  | 2 | 18V |
| positioner_type | operating mode : 0 - “disabled” - no motor, 1 - “ diseqc 1.2 ” positioner, 2 - “USALS”, do not display this field |
| motor_ type | exchange protocol : "disabled" - no motor, "diseqc 1.2", "diseqc 1.3" the correct print is: positioner_type_name[ motor _type ] |
| toneburst | tone package: |
|  | 0 | off |
|  | 1 | satellite 'A' |
|  | 2 | satellite 'B' |

Example: http://192.168.1.56/public?command=returnSATList

Answer:

{

"sat_num": 63,

"sat_list": [

{

"sat_degree": "85.0",

"direction": "E",

"lnb_type": 2,

"lnb_low_freq": 9750,

"lnb_high_freq": 10600,

"sat_name": ". Telekarta",

"sat_id": 0,

"tone": 0,

"v12": 0,

"diseqc10_type": 0,

"diseqc10_port": 0,

"motor_position": 0,

"diseqc11_type": 0,

"diseqc11_port": 0,

"positioner_type": 0,

"lnb_power": 0,

"toneburst": 0

}, … ] , "Ret_code": "DB_NO_ERR" }

- returnTPList

Request a list of frequencies for a given satellite. If the sat_id parameter is not set, the entire list of frequencies is returned.

| Parameter field | Description |
| --- | --- |
| sat_id | unique internal satellite number (see returnSATList.sat_list[ x ].sat_id ) |

| Reply field | Description |
| --- | --- |
| ret_code | method error codes: |
|  | DB_NO_ERR | read from the database without errors |
|  | SYS_NO_SAT_LIST_ERR | no satellite base |
|  | DB _ NO _ SAT _ ERR | invalid satellite ID |
|  | SYS_MEM_ERR | no memory for json text |
| tp_num | number of frequencies in the satellite base |
| tp_list | frequency list |
| freq | frequency, MHz |
| sr | transponder symbol rate |
| polarity | polarization: 0 - horizontal, 1 - vertical |
| id | unique internal transponder number |
| sat_id | unique internal satellite number |
| pat_version | reserved |
| scrambled | reserved |
| tone | reserved |
| nim_type | broadcast standard: 0 - unknown , 1 - DVBS , 2 - DVBS2 |
| enable_lcn | reserved |
| emm_num | reserved |
| emm_list | reserved |
| ca_sys_id | reserved |
| emm_pid | reserved |

Example: http://192.168.1.56/public?command=returnTPList&sat_id=0

Answer:

{

"tp_num": 2,

"tp_list" : [

{

"freq": 11720,

"sr": 28800,

"polarity": 0,

"id": 1

},

{

"freq": 11760,

"sr": 28800,

"polarity": 0,

"id": 2

}

],

"ret_code": "DB_NO_ERR"

}

- createReport

Start creating of a satellite report, the current progress of the process is periodically streamed in json format.

| Parameter field | Description |
| --- | --- |
| sat_id | unique internal satellite number (see returnSATList.sat_list [x].sat_id) |
| user_longtitude | longitude of the dish installation: “N” for >= 0, “S” for < 0 |
| user_altitude | latitude of the dish installation: “E” for >= 0, “W” for < 0 |
| lnb_3d_serial | 3D converter serial number (10 characters) |
| lnb_alfa | averaged angle of inclination, the X axis, degrees; 360.0 means that the 3D converter is not connected |
| lnb_beta | averaged angle of inclination, the Y axis, degrees |
| lnb_gamma | averaged angle of inclination, the Z axis, degrees |
| lnb_alfa_correction | X-axis calibration, degrees |
| lnb_beta_correction | Y-axis calibration, degrees |
| lnb_gamma_correction | Z-axis calibration, degrees |
| lnb_alfa_ripples | maximum ripple amplitude, the X axis, degrees |
| lnb_beta_ripples | maximum ripple amplitude, the Y axis, degrees |
| lnb_gamma_ripples | maximum ripple amplitude, the Z axis, degrees |
| vendor | dish manufacturer |
| model | dish model |
| diameter | dish diameter |
| offset | dish elevation offset, which is individual for each model |
| user | “fixed_offset” – preset offset from the base; “measured_offset” – custom offset in the base; “unknown_offset” – the dish is included in the base, but the offset is not specified |
| file_type | report type: "basic" - basic report, "dish_ethalon" - a report taken near the dish, "stb_ethalon" - a report taken at the usual stb location |

| Reply field | Description |
| --- | --- |
| scan_progress | percentage of report generation progress |
| tune_mode | operating mode: 2 - report generation |

Example: http://192.168.1.56/public?command=createReport&sat_id=0

- scanChannels

Start scanning channels in different modes. If the scanning mode is “blindscan” or “sat”, then you can send the “sat_id” field without “tp_id”, if “tp”, then “sat_id” is not needed. When transmitting the “ sat_id ” and “ tp_id ” fields in any mode, the ones required for the specified mode will be used.

| Parameter field | Description |
| --- | --- |
| sat_id | unique internal satellite number (see returnSATList.sat_list [x].sat_id) |
| tp_id | unique internal transponder number (see returnTPList.tp_list [x]. id) |
| free_only | “true” - only open channels, “false” - all channels |
| nit | “true” - network search, “false” - no network search |
| channel_type | type of scanned channels: |
|  | all | scan all channels |
|  | tv | TV channels only |
|  | radio | radio channels only |
| mode | scan mode: |
|  | blindscan | blind scan on satellite |
|  | sat | search by satellite transponders from the base |
|  | tp | search by one transponder |
|  | dvbt_full | All terrestrial TP search |
|  | dvbt_tp | One terrestrial TP search |
|  | dvbc_manual | One cable TP search |

| Reply field | Description |
| --- | --- |
| ret_code | method error codes: |
|  | NO_ERR | executed without errors |
|  | STREAMING_ERR | the receiver is busy streaming the channel |
|  | PARAM_ERR | error in the input parameters field |
| channel_scan_progress | channel scan progress percentage |
| tune_mode | operating mode: 4 - channel scanning |
| tp_num | number of scanned frequencies |
| tv_num | number of TV channels found |
| radio_num | number of radio channels found |
| full_db_flag | 1 - the channel database is full, 0 - enough space for channels |
| finished_flag | scan finished |
| stopped_flag | scan is stopped |
| destroyed_flag | freeing GUI resources completed |
| start_err | 1 - error starting the scanning process, 0 - start successful. You need to wait one second for status 1. |

Example: http://192.168.1.56/public?command=scanChannels&sat_id=404&tp_id=405&&free_only=false&nit=false&channel_type=all&mode=tp

- updateConfig - HTTP POST

Loading the settings into the receiver.

| Reply field | Description |
| --- | --- |
| ret_code | method error codes: |
|  | NO_ERR | read without errors |
|  | STB_BUSY_ERR | the receiver is busy executing another request |
|  | DB_SATID_TAG_ERR | invalid parameter field |
|  | DB_NO_SAT_ERR | invalid satellite ID |
|  | SYS_MEM_ERR | no memory for json text |
| parser_err | parser json error number: |
|  | 0 | no mistakes |
|  | -1 | error parsing json fields |
|  | -2 | json parse error |
|  | -5 | set parameters error |
|  | -54 | none of the parameters changed |

| Settings field | Description |
| --- | --- |
| mediacenter | media center menu settings |
| record | disc recording settings after pressing the pause button while watching a program |
| timeshift | program recording: “true” - enabled, “false” - disabled |
| disk_partition | disc name for video recording (“C”, “D”) |
| network | network settings |
| wifi | network settings when connected to TV via HDMI |
| essid | access point name |
| password | password |
| encrypt | encryption type : "none" (no encryption) , "WEP", "WPA1", "WPA2" or "auto", if you want determine automatically; it will take less than a second extra time the first time you connect after applying the settings |
| auto_connect | settings for connecting to the network if there is no TV |
| stb_name | the name of the receiver to find it on the network |
| essid | access point name |
| password | password |
| system | system settings |
| language | language settings |
| osd | menu |
| first_audio | first audio track |
| secondary_audio | second audio track |
| subtitles | subtitles |
| audio_video | audio and video setup |
| tv_system | TV system: “PAL”, “NTSC”, “auto” |
| resolution | resolution: “480i”, “576i”, “576p”, “720p” , “1080i”, “1080p”, “auto” |
| aspect | aspect ratio: "auto", "4:3LetterBox", "4:3PanScan", "16:9" |
| effects | menu video effects: "standard", "default", "vivid" |
| audio_out | audio output format: "LPCM", "BS", "SPDIF", "auto" |
| time | time settings |
| gmt | enable GMT : “true” - enabled, “false” - disabled |
| timezone | time zone shift, use the recording format: “ 04:30 ” or “ - 04:30 ” |
| summertime | enable daylight saving time : “true” - enabled, “false” - disabled |
| messages | messages settings |
| subtitles | subtitles: “true” - enabled , “false” - disabled |
| infobanner_time | channel information display time, seconds |
| infobanner_transperancy | menu transparency, percentages |
| favorites | favorites list (16 lines) : |
|  | name | list name |
|  | unicode | "true" - unicode format for name ("\u041D") , “false” - ASCII format |
|  | comment | hint language and list name: "rus: News", for example |
| settings | satellite settings |
| usals_pos | geographical dish location: |
|  | longtitude | latitude |
|  | latitude | longitude |
| lnb_list | list of built-in LNB local oscillators , they cannot be changed |
| lnb_low _ freq | lower local oscillator frequency, MHz |
| lnb_high _ freq | upper local oscillator frequency, MHz |
| unicable | LNB type : |
|  | disabled | usual |
|  | A | unicabel protocol A |
|  | B | unicabel protocol B |
| dvbt_info | Terrestrial search settings |
|  | country | Country selection to form a grid of frequencies search |
| satellite_list | satellite list |
| slot_index | slot index for storing satellite settings, the same as in the receiver menu |
| sat_id | unique satellite internal number, read only |
| replace | always “true” - allow replacing slot settings in place of the previous ones |
| sat_degree | satellite position, degrees |
| direction | direction to the satellite: 'E' - east , 'W' - west |
| name | user defined satellite name |
| setup | objects with satellite settings |
| lnb_low _ freq | lower local oscillator frequency, MHz |
| lnb_high _ freq | upper local oscillator frequency, MHz |
| unicable | unicable settings object |
| type | unicable type : |
|  | disabled | disabled |
|  | A | unicable protocol A |
|  | B | unicable protocol B |
| channel | channel number |
| frequency | center frequency |
| diseqc1.0 | DISEQC version 1.0 port number, values: 1- 4 or disabled |
| diseqc1. one | DISEQC version 1.1 port number, values: 1-16 or disabled |
| toneburst | tone burst: |
|  | off | off |
|  | A | satellite ' A ' |
|  | B | satellite ' B ' |
| v 12 | output (option) 12V: “on” - enabled, “off” - disabled |
| tone | tone: “on” - on, “off” – off; not used for universal LNB |
| power | converter power settings: |
|  | auto | depending on transponder settings |
|  | 13V | to set 13V |
|  | 18V | to set 18V |
| motor | motor settings object |
| mode | operating mode: “disabled” - no motor, “diseqc 1.2” positioner , “USALS” |
| type | exchange protocol: "disabled" - no motor, "diseqc 1.2", "diseqc 1.3" |
| position | DiSEqC1.2 positioner position number |

Example: http://192.168.1.56/public?command=updateSettings

Next, we pass the json settings in the POST request body, an example in the stb_config_example.json file

- smartcardInfo

Getting information about the smartcard.

| Reply field | Description |
| --- | --- |
| ret_code | method error code: |
|  | NO_ERR | read without errors |
|  | NO_SUPPORT_ERR | smartcard not supported |
| smartcard_info_progress | To get smartcard information status: |
|  | 0 | poll started |
|  | 1 | number read |
|  | 2 | number and subscriptions read |
| tune_mode | operating mode: 5 - smartcard polling |
| status_code | if the field is present, the error is “SYS_NOT_STARTED_ERR” and that means the startEvents method was used without specifying the operating mode |
| smartcard_info | smartcard information object |
| serial | smartcard serial number |
| version | smartcard version |
| name | provider name |
| entitle_info | smartcard subscriptions list |
| type | type of subscription: "Package" – usual subscriptions, "PPV" - on request |
| class | subscription class |
| id | provider id |
| start_time | subscription start date |
| end_time | subscription end date |
| name | provider name |

Example: http://192.168.1.56/public?command=cardInfo

Status example:

{

"card_info_progress": 2,

"tune_mode": 5,

"card_info": {

"serial": "2777777777",

"version": "64",

"name": "Test card 1"

},

"entitle_info" : [

{

"type": "Package",

"class": "010000AA",

"id": "1010",

"start_time": "01/09/2020"

"end_time": "31/09/2020"

"name": "Test card 1"

},

{

"type": "Package",

"class": "010000AA",

"id": "1010",

"start_time": "01/08/2020"

"end_time": "31/08/2020"

"name": "Test card 1"

},

{

"type": "Package",

"class": "01000FFF",

"id": "1020",

"start_time": "01/01/1990",

"end_time": "01/01/1990",

"name": "Test card 1"

},

{

"type": "Package",

"class": "0100FFFF",

"id": "1030",

"start_time": "01/01/1990",

"end_time": "01/01/1990",

"name": "Test card 1"

}

]

}

- channelList

Getting a list of all channels in json format if the 'type' parameter is not specified. The same response fields are used to send the channel list back to the receiver using the updateSettings method.

| Parameter field | Description |
| --- | --- |
| type | tv | TV channels only |
|  | radio | radio channels only |

| Reply field | Description |
| --- | --- |
| ret_code | method error code: |
|  | NO_ERR | no errors while creating the list |
| channel_num | number of channels in the list |
| channel_list | channel list object |
| name | channel name in unicode format, example "\u041C" |
| fav_group_flag | favorite group bitmask: bit 0 - “FAV 1”, bit 15 - “FAV 16” etc. in decimal format, 16 groups in total example: 20dec = 14hex = 00010100bin - FAV 3 and FAV 5 groups selected |
| flag | channel settings flags: |
|  | tv | 1 - TV channel, 0 - radio |
|  | lock | 1 - channel is blocked, 0 – is not blocked |
|  | skip | 1 – the channel is skipped, 0 – is not skipped |
|  | hide | 1 - the channel is hidden in the lists, 0 – is not hidden (if “hide” is 1 - "skip" is also 1) |
|  | t2mi | 1 - t2mi support, 0 - no support |
| volume | default channel volume |
| audio_channel | the current audio channel index from the “audio” list |
| scrambled | 1 - the channel is encrypted, 0 – opened |
| audio_ch_num | the number of audio streams per channel |
| audio_track | audio track settings: 0 - stereo, 1 - left channel, 2 - right channel |
| service_type | service type: 0 - SD ,17 - HD ,22 - undefined service_type description (0x48) 0x00 reserved for future use 0x01 digital television service 0x02 digital radio sound service 0x03 Teletext service 0x04 NVOD reference service 0x05 NVOD time-shifted service 0x06 mosaic service 0x07 PAL coded signal 0x08 SECAM coded signal 0x09 D / D2-MAC 0x0A FM Radio 0x0B NTSC coded signal 0x0C data broadcast service 0x0D reserved for Common Interface Usage [17] 0x0E RCS Map (see EN 301 790 [35]) 0x0F RCS FLS (see EN 301 790 [35]) 0x10 DVB MHP service 0x11 to 0x7F reserved for future use 0x80 to 0xFE user defined 0xFF reserved for future use |
| video_type | video type: "Elementary stream types" https://en.wikipedia.org/wiki/Program-specific_information, locally in a file es_types.txt |
|  | 0 | MPEG | 5 | MPEG_ES | 9 | VC1 | 13 | H263 |
|  | 1 | H264 | 6 | H264_ES | 10 | VP8 | 14 | HEVC |
|  | 2 | AVS | 7 | AVS_ES | 11 | RV3 | 15 | VC1SMP5 |
|  | 4 | MPEG4 | 8 | MPEG4_ES | 12 | RV4 | 16 | UNKNOWN |
| audio_channel_modified | reserved |
| pid | object with ES PIDs |
| video | video stream |
| pcr | main frequency reference |
| pmt | program managment table |
| id | object with unique identifiers |
| channel | unique internal channel number (not used) |
| sat | unique internal satellite number |
| tp | unique internal transponder number |
| sid | channel id |
| original_network | broadcast network unique identifier |
| stream | broadcast stream identifier |
| cas | conditional access system, for example, 0x500 = 1280dec (viaccess) https://en.wikipedia.org/wiki/Conditional_access |
| plp | PLP identifier |
| t2mi_plp | T2MI identifier |
| default_order | default sequence number |
| logical_num | logical channel number (LCN used for T2) |
| ecm_num | number of ECM PIDs in the ecm_pid list |
| age_limit | reserved |
| audio_ad_channel | reserved |
| audio_ad_channel_num | reserved |
| ecm_pid | list of ECM PIDs, the number is specified in the ecm_num field |
| audio | audio channels list in the program |
| pid | audio stream identifier |
| type | audio format: |
|  | 0 | PCM | 5 | EAC3 | 10 | AMR_IFX | 111 | SPDIF_DTS |
|  | 1 | MP1 | 6 | AAC | 107 | SPDIF | 112 | UNKNOWN |
|  | 2 | MP2 | 7 | AAC_V2 | 108 | DOLBY_CONVERT |  |  |
|  | 3 | MP3 | 8 | DRA | 109 | SPDIF_AC3 |  |  |
|  | 4 | AC3_VSB | 9 | WMA | 110 | SPDIF_EAC3 |  |  |
| language_index | internal language index; possible languages https://www.loc.gov/standards/iso639-2/php/English_list.php ; mapping the language to the index in the language_index.txt file |
| audio_type | 1 - CLEAN_EFFECTS , 2 - HEARING_IMPAIRED , 3 - VISUAL_IMPAIRED_COMMENTARY |

Example: http://192.168.1.56/public?command=channelList

Sample response in channel_list_example.json file.

- getConfig

Getting receiver settings. The fields are similar to the method updateConfig.

Example: http://192.168.1.56/public?command=getConfig

- upgradeSoftware - HTTP POST

Upgrading STB firmware. If the parameter field is not specified, then the default mode is “main”.

| Parameter field | Description |
| --- | --- |
| upgrade_mode | update mode: “main ” - update only the code; "all " - update of all flash memory with erasing of channels, reports and settings. |

| Reply field | Description |
| --- | --- |
| ret_code | method error codes: |
|  | NO_ERR | read without errors |
|  | BIN_FILE_ERR | wrong firmware file |
|  | STREAMING_OR_REPORT_ERR | receiver in report creation or channel streaming mode |
| burn_progress | the progress of the receiver upgrading process, % |
| event_id | reserved |
| tune_mode | operating mode: 6 - receiver is upgrading |
| burn_sm | reserved |

Example: http://192.168.1.56/public?command=upgradeSoftware&upgrade_mode=all

Sample code in the upgrade_test.html file.

- commonEvent

Enabling standard event mode for the startEvents method.

| Reply field | Description |
| --- | --- |
| ret_code | method error code: NO_ERR - no errors |
| tune_mode | operating mode: 7 - standard events |
| card_inserted | Check if the card is inserted or not: “true” - inserted, “false” - not inserted |

Example: http://192.168.1.56/public?command=commonEvent

- formatEmbeddedPartition

Format embedded flash memory partition.

| Поле параметра | Описание |
| --- | --- |
| partition | partition letter |

| Поле ответа | Описание |
| --- | --- |
| ret_code | method error code: |
|  | FS_NO_ERR | formatted without errors |
|  | FS_FORMAT_ERR | format error |

Example:

http://192.168.1.56/public?command=formatEmbeddedPartition&partition=e

Исходный текст

имя бинарного файла отчета с заменойраcширениянаjson

Предложить лучший вариант перевода